GYPSUM CEMENT UNDERLAYMENT

RECOMMENDED SPECIFICATION FOR MAXXON( GYP-CRETE HIGH PERFORMANCE FLOOR UNDERLAYMENT OVER VINYL ASBESTOS TILE

PART 1 GENERAL

1.01    SUMMARY

- This is the recommended specification for Maxxon( Gyp-Crete® High Performance Floor Underlayment for topping vinyl asbestos tile.

  - Maxxon( Gyp-Crete® High Performance Underlayment

  - Division 3 Section-Concrete: “Cast Underlayment” and “Gypsum Cement Underlayment”

  - Division 9 Section-Finishes: “Acoustic Treatment”

  - REFERENCES

- Underwriters Laboratory 		Fire Resistance Volume 1

www.ul.com

- GREENGUARD Certified	GREENGUARD and GREENGUARD Gold Certified

www.greenguard.org

- ASTM E336 and E1007		Field Sound Transmission Class (F-STC), Field

Impact Insulation Class (F-IIC)

- ASTM E90 and E492		Sound Transmission Class (STC), Impact Insulation

Class (IIC)

- ASTM C472M			Compressive strength of gypsum concrete

- ASTM F2170				Standard Test Method for Determining Relative

Humidity in Concrete Floor Slab

- ASTM F2419				Standard Test Method for Installation of Thick

Poured Gypsum Concrete and Preparation of

Surface to Receive Resilient Flooring

- ASTM F2678				Standard Practice for Preparing Panel Underlayments,

Thick Poured Lightweight Cellular Concrete Underlayments, and Concrete Subfloors with Underlayment Patching Compounds to Receive Resilient Flooring

- TCNA F 180				Tile Council of North America Installation Handbook

www.tileusa.com

- NWFA					National Wood Flooring Association Instructions

www.nwfa.org

- Finished Floor Goods Procedures	Maxxon Procedures for Attaching Finished Floor

Goods to Maxxon Underlayments

www.maxxon.com

1.03    SUBMITTALS

- Product Data: Submit sale sheets Dura-Cap Sales Sheet, Acousti-Mat TDS, Acousti-Mat Perimeter Isolation Strips Spec Sheet, Procedures for Attaching Finished Floor Goods to Maxxon Underlayments, and Maxxon’s Building Conditions Guide with project materials clearly identified for each required product or system.

- Acoustical Data: Submit sound tests according to IBC code criteria ASTM E492 (IIC) and ASTM E90 (STC) or ASTM E1007 (F-IIC) and E336 (F-IIC).

- Code Approvals: See www.maxxon.com for the current list of code approvals.

1.04     SYSTEM REQUIREMENTS

- Performance Requirements:

  - Maxxon( Gyp-Crete® High Performance Floor Underlayment

    - Compressive Strength (Modified ASTM C472):

Typical range of 3,000 – 4,000 psi (20.7 - 27.6 MPa)

    - Density 115-125 lbs./ft3 (1842-2002 kg/m3)

**********This product may contribute to USGBC LEED Credits (MR 3; EQ 2, 4) **********

Potential USGBC LEED Credit Contribution:

a. MR Credit 3: Building Product Disclosure and Optimization - Sourcing Raw Material

b. EQ Credit 2: Low Emitting Materials.

c. EQ Credit 4: Indoor Air Quality Assessment.

Contact Maxxon Corporation for specific details.

******************************************************************************************************

  - Sound Control – 2009 International Building Code: Section 1207.2 & .3

    - Minimum Sound Transmission Class, 50 STC (45 if field tested) – Section 1207.2

      - ASTM E90 and E336

    - Minimum Impact Insulation Class, 50 IIC (45 if field tested) – Section 1207.3

      - ASTM E492 and E1007

1.05    QUALITY ASSURANCE

- Performance Standards:

  - All materials, unless otherwise indicated, shall be manufactured by Maxxon Corporation and shall be installed in accordance with its current printed directions and by a Maxxon Corporation Authorized Applicator.

  - Underlayment mix shall be tested for a slump using a 2" (i.d.) x 4" (50 mm x 101 mm) cylinder resulting in a patty size of 9" (229 mm) plus or minus 1 inch (25 mm) diameter.

  - Compressive strength tested in accordance with ASTM C472M.

  - DELIVERY, STORAGE AND HANDLING

- All materials shall be delivered in their original unopened packages and protected from damage and exposure from the elements. Damaged or deteriorated materials shall be removed from the premises.

1.07     PROJECT CONDITIONS

- Before, during and after installation of product, building interior shall be enclosed, with adequate ventilation and heat maintained at a temperature above 50° F (10°C) to allow for drying of product.

PART 2 GENERAL

2.01     PRODUCTS AND MANUFACTURERS

A.  Manufacturer: Maxxon Corporation, Hamel, MN. Telephone: (800) 356-7887

2.02    MATERIALS

- Proprietary products/systems: Poured flooring underlayment and topping products, including the following:

  - Maxxon( Gyp-Crete® High Performance Floor Underlayment

- Proprietary products/systems: Optional Sound Control that does not negate the fire rating and is specified in UL design. Acoustical performance is dependent on system design and construction.

  - Maxxon Acousti-Mat® 1/8 Sound Mat

  - Maxxon Acousti-Mat® 1/4 Sound Mat

  - Maxxon Acousti-Mat® 1/4 Premium Sound Mat

  - Maxxon Acousti-Mat® 3/8 Sound Mat

  - Maxxon Acousti-Mat® 3/8 Premium Sound Mat

  - Maxxon Acousti-Mat® 3/4 Sound Mat

  - Maxxon Acousti-Mat® 3/4 Premium Sound Mat

- Maxxon Acousti-Mat Perimeter Isolation Strips as manufactured by Maxxon Corporation, Hamel, MN

- Maxxon Acousti-Mat Tape as manufactured by Maxxon Corporation, Hamel, MN

- Maxxon Floor Primer:

  - Material Standard: Comply with specifications outlined in manufacturer's Design and Installation Guide for wood.

- Mix Water:

  - Material Standard: Potable, free from impurities and from a domestic source.

- Sand Aggregate:

  - Sand shall meet Maxxon Sand Specification 101.

- Maxxon Commercial Gypsum Overspray:

  - Seal all areas that receive glue down floor goods with Maxxon Commercial Gypsum Overspray according to manufacturer's specifications.

- Maxxon Commercial Multi-Use Acrylic Primer (Alternate to Overspray):

  - Seal all areas that receive glue down floor goods with Maxxon Commercial Multi-Use Acrylic Primer according to manufacturer’s specifications.

- Maxxon Commercial Isolate

PART 3 EXECUTION

3.01     EXAMINATION

- Site Verification of Conditions:

  - Installation shall not begin until the building is enclosed, including roof, windows, doors, and any other apertures.

  - Concrete substrate shall be structurally sound, and dry. Contractor shall clean subfloor to remove mud, oil, grease, and other contaminating factors before arrival of the authorized applicator.

3.02     REQUIREMENTS

- Leak Prevention:

  - Fill cracks and voids in subfloor where leakage of slurry could occur.

- Priming subfloor:

  - Prime substrate according to manufacturer's recommendations.

- Application:

  - Install in accordance with reference standards and manufacturer's instructions.

3.03    GENERAL INSTALLATION REQUIREMENTS

- Maxxon Commercial Isolate

  - Install per manufacturer's recommendations

- Mixing Proportions:

  - General Requirements: Mix proportions and methods shall be in strict accordance with product manufacturer recommendations.

- Application:

    - Place Gyp-Crete High Performance from 3/8’ (10 mm) minimum over vinyl asbestos tile.  Over concrete, it can be featheredged.  Spread and screed the Gyp-Crete High Performance to a smooth surface.  Except at authorized joints, place Maxxon( Gyp-Crete® High Performance as continuously as possible until application is complete so that no Gyp-Crete High Performance slurry is placed against Gyp-Crete High Performance product that has obtained its initial set.

- Drying:

  - The general contractor must provide and maintain correct environmental conditions to keep the building clean and dry, and protect against infestation of moisture from a variety of potential sources.  The general contractor must supply mechanical ventilation and heat if necessary to remove moisture from the area until the Maxxon( Gyp-Crete® High Performance is dry.

  - Protection from Heavy Loads:  During construction, place temporary wood planking over Maxxon( Gyp-Crete® High Performance wherever it will be subject to heavy wheeled or concentrated loads.

  - PREPARATION FOR INSTALLATION OF GLUE DOWN FLOOR GOODS

- Sealing:

  - Seal all areas that receive glue down floor goods with Maxxon Commercial Gypsum Overspray or Maxxon Commercial Multi-Use Acrylic Primer according to the Maxxon Corporation's specifications.  Any floor areas where the surface has been damaged shall be cleaned and sealed regardless of floor covering to be used.  Where floor goods manufacturers require special adhesive or installation systems, their requirements supersede these recommendations.

  - Maxxon Commercial Fortify can be used over Maxxon underlayments in low traffic areas such as utility rooms, storage rooms and closets, as a protective surface.

- Moisture Testing:

  - Follow the respective floor goods manufacturers’ recommendations for relative humidity requirements.  When manufacturer does not have a relative humidity requirement, refer to Maxxon’s Procedures for Attaching Finished Floor Goods to Maxxon Underlayments brochure.

- Finished Floor Goods:

  - There are many reference standards for the installation procedures and recommendations for finished flooring applications over gypsum underlayments.  These include instructions of the manufacturers of the finished flooring, adhesives and thin-set as well as national agency reference standards.  The national standards are listed below:

| Flooring Type | Reference Standard |
| --- | --- |
| Resilient | ASTM F2419 |
| Ceramic Tile | TCNA F180 |
| Wood | NWFA Instructions |

See Maxxon Corporation's Procedures for Attaching Finished Floor Goods to Maxxon Underlayments brochure for guidelines for installing finished floor goods.  This procedure is not a warranty and is to be used as a guideline only.

END OF SECTION